 Arduino-Arduino communication through the serial ports
- Serial is used for communication between the Arduino board and a computer or other devices
- All Arduino boards have at least one serial port
- Requires only 2 pins
- Communication either half-duplex or full-duplex

---
Remove Connections Before Upload Code

---
Transmitter Receiver

---
Control Rx from Tx

---
Software Serial
- Why remove wires before uploading code ?
- serial port is connected to the computer through the USB cable
- Its not possible to upload the code when it is already connected to the another arduino
- to send the commands from Tx to be transfered to the Rx , Software Serial Library is used

---
Command Rx from Tx

---
SPI Communication
- Tx , Rx are Asynchronous – no control over when the data is sent or receive
- SPI is a Synchronous data bus
- It uses separate lines for data and clock to keep both sides in perfect sync