Introduction to Arduino

---
What is Arduino ?
The Arduino is a tiny computer system that can be programmed with your instructions to interact with various forms of input and output

---
Quick Tour	of Arduino
USB Connector
- Connects Arduino to Computer
- To Supply Power
- Upload Instructions to Arduino
- Send and Receive Data

---
Quick Tour	of Arduino
- Power the Arduino with DC 9-12V plug

---
Quick Tour Arduino
MicroController
- Brain of the Arduino
- Executes Instructions
- Contains Memory

---
Quick Tour Arduino
Analog Inputs
- Six Analog In Pins
- Measure Electrical Signals vary in voltage

---
Quick Tour of Arduino
- Power Connections
- External RESET

---
Quick Tour of Arduino
Digital Input and Output Pins
- Detect the prescence of signal or Can Generate on Command
- ‘ ~ ‘ Labelled pins can generate varying electrical signal

---
Quick Tour of Arduino
On Board Led’s
- TX, RX light up when Data being Transmitted and Received
- L is connected to Digital Pin 13

---
Software - Download
Arduino.cc/en/Main/Software
Select Installer

---
Installation
- Double click on the Downloaded Exe File
- Allow OS to install Drivers

---
installation

---
Installation - Driver
- Connect Arduino to Computer using USB Cable
- Open Device Manger
- Look under Ports
- Note Arduino UNO COM port

---
IDE – Test Run
- Double Click on the Arduino Icon in Desktop
- The Tab is known as Sketch
- It Contains the program that tells your board what to do

---
 Test Run - Blink It
Go to File->Examples-> Basics-> Blink and click on it

---
 Test Run - Blink It
- Select Board type in Tools -> Board
- Select UNO
- Select COM port noted Previously in Tools -> Port

---
Test Run - Upload
- Click the upload button
- you should see the RX and TX leds on the board flashing
- After few seconds on board led blinks

---
Introduction to Arduino Programming

---
Structure
- Every Program must contain these two functions
- Setup is preparation
  it is the first function to run and run only once
- Loop is execution
  it is executed continuesly

---
Fuctions
- Function is block of code that has a name and a block of statements when the function is called
- Setup() and loop() are built-in functions
  - we will talk about custom functions later

---
Basic Syntax
- Each Statement Ends with semicolon “;”
  int a = 13;
- Curly braces always come in pairs; they are used to define the start and end of functions, loop, conditional statements
- // is used for single line comment
- /* */ used to wrap multiline comment

---
Hello World
- Usb is used to send and Receive Data Serially
- Serial Port / Com port talks with certain speed, called Baudrate

---
Hello World
Serial.begin(9600) basically tells the Arduio to start talking over serial port at a speed of 9600 baud
Baudrate – Bits per second

---
Hello World
- Serial.print tells the Arduino to send a text line to Serial port
- Notice the Semicolon (;) - every statement must end with semicolon

---
Select Port and Board
- Select Board type in Tools -> Board
- Select UNO
- Select COM port noted Previously in Tools -> Port

---
Upload & Open Serial Monitor
- Upload the Sketch
- Observe the tx & rx blinking on Board
Click on the magnifying glass to open Serial Monitor

---
Try with Differnt Baudrates by changing in Serial.begin and Serial Monitor

---
Print vs println
“Arduino “ Starts in new line But “From” is on same ine

---
Setup vs loop
Statement in loop is repeting

---
Delay
- Delay Pauses the program for the amount of time (in miliseconds) specified as parameter
- it brings all other activities to a halt

---
Variables
- A variable is a place to store a piece of data
- It has a name, a value, and a type
  int a = 13;
- creates a variable whose name is a, whose value is 13, and whose type is int

---
Variable types & Rules
- consist of any letters (a to z and A to Z)
- contain the numbers 0 to 9, but may not start with a number, e.g. 3var is not allowed, but var3 is allowed
- Variables may not have the same names as Arduino language keywords, e.g. you can not have a variable named int
- Variables must have unique names i.e. you can not have two variables with the same name
- Variable names are case sensitive, so Count and count are two different variables
- Variables may not contain any special characters, except the underscore (_), e.g. top_score
Type	Description
int	Integer max size is 2^8
float	Floating point value
char	Character
String	String

---
Variable Scope
- scope is the lifetime and visibility a variable has in a program
  - Global : A variable with global scope is visible from its point of definition to the end of the file in which it is defined
  - Local : A variable with local scope extends from its point of definition to the end of the function block in which it is define

---
Arithmetic operators
Symbol	Name	Example	Explanation
=	assignment	Led = 13	Store the value 13 at variable led
+	addition	A = B + C	Add the variable B,C and assign the result to C
-	subtraction	A = B - C	Subtract C from B and assign the result to A
*	multiplication	A = B*C	Multiply B and C and assign the result to A
/	division	A = B/C	Divide B with C and assign the result to A
%	modulo	A = B%C	Calculate the Remainder of division B/C and assign it to the A

---
Comparison Operators
Result of statement with comparision operator is either TRUE or FALSE
        0 < x < 1 is invalid
Symbol	Name	Example	Explanation
==	Is equal to	X == Y	X is equal to y
!=	Not equal to	X != Y	X is not equal to Y
<	Less than	X < Y	X less than Y
>	Greater than	X > Y	X greater than Y
<=	Lessthan or equal to	X <= Y	X less than or equal to Y
>=	Greater than or equal to	X >= Y	X greater than or equal to Y

---
Boolean Operators
Symbol	Name	Example	Explanation
&&	Logical AND	X>Y && Y<Z	True only if both conditions are true
||	Logical OR	X>Y || Y< Z	True if any one of condition is true
!	NOT	!X	Invert the boolean value X

---
Lets start Tinkering